## Slide 1
Computer Organization and Architecture
Lecture 22 Caches
Jihe Wang
wangjihe@nwpu.edu.cn

## Slide 2: The Big Picture: Where are We Now?
0
The Five Classic Components of a Computer
Today’s Topics:
  Recap last lecture
  Simple caching techniques
  Many ways to improve cache performance
  Virtual memory?
Control
Datapath
Memory
Processor
Input
Output

## Slide 3: Today’s Topic
00
01. The Problems in Memory
02. Locality and Cache
03. Memory Hierarchy
04. Cache Details
05. Performance Analysis

## Slide 4: Memory Gap
1.1

## Slide 5: Ideal Memory
1.2
Zero access time (latency)
Infinite capacity
Zero cost
Infinite bandwidth (to support multiple accesses in parallel)

## Slide 6: Memory Access Latency VS processor cycle
1.3
Memory delay vs. cycle time vs. average stages.

## Slide 7: Example Time Scale of System Latencies
1.3

## Slide 8: The Problems in Memory
1.4
Bigger is slower
  SRAM, 512 Bytes, sub-nanosec
  SRAM, KByte~MByte, ~nanosec
  DRAM, Gigabyte, ~50 nanosec
  Hard Disk, Terabyte, ~10 millisec
Faster is more expensive (dollars and chip area)
  SRAM, < 10$ per Megabyte
  DRAM, < 1$ per Megabyte
  Hard Disk < 1$ per Gigabyte
  These sample values scale with time
Other technologies have their place as well
  Flash memory, PC-RAM, MRAM, RRAM (not mature yet)

## Slide 9: Today’s Topic
00
01. The Problems in Memory
02. Locality and Cache
03. Memory Hierarchy
04. Cache Details
05. Performance Analysis

## Slide 10: Locality
2
One’s recent past is a very good predictor of his/her near future.
Temporal Locality: If you just did something, it is very likely that you will do the same thing again soon
  since you are here today, there is a good chance you will be here again and again regularly
Spatial Locality: If you did something, it is very likely you will do something similar/related (in space)
  every time I find you in this room, you are probably sitting close to the same people

## Slide 11: Memory Locality
2.1
A “typical” program has a lot of locality in memory references
  typical programs are composed of “loops”
Temporal: A program tends to reference the same memory location many times and all within a small window of time
Spatial: A program tends to reference a cluster of memory locations at a time
  most notable examples:
    1. instruction memory references
    2. array/data structure references
    A loop example.

## Slide 12: Memory Locality
2.1

## Slide 13: Caching Basics: Exploit Temporal Locality
2.2
Idea: Store recently accessed data in automatically managed fast memory (called cache)
Anticipation: the data will be accessed again soon
Temporal locality principle
  Recently accessed data will be again accessed in the near future
  This is what Maurice Wilkes had in mind:
    Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.
    “The use is discussed of a fast core memory of, say 32000 words as a slave to a slower core memory of, say, one million words in such a way that in practical cases the effective access time is nearer that of the fast memory than that of the slow memory.”

## Slide 14: Caching Basics: Exploit Spatial Locality
2.3
Idea: Store addresses adjacent to the recently accessed one in automatically managed fast memory
  Logically divide memory into equal size blocks (disk->mem.)
  Fetch to cache the accessed block in its entirety (mem.->cache)
Anticipation: nearby data will be accessed soon
Spatial locality principle
  Nearby data in memory will be accessed in the near future
    E.g., sequential instruction access, array traversal

## Slide 15: The Bookshelf Analogy
2.4
Book in your hand
Desk
Bookshelf
Boxes at home
Boxes in storage
Recently-used books tend to stay on desk (when to swap/how to pick?)
  Comp Arch books, books for classes you are currently taking
  Until the desk gets full
Adjacent books in the shelf needed around the same time (How to place/layout?)
  If I have organized/categorized my books well in the shelf

## Slide 16: Caching in a Pipelined Design
2.5
The cache needs to be tightly integrated into the pipeline
  Ideally, access in 1-cycle so that dependent operations do not stall
High frequency pipeline  Cannot make the cache large
  But, we want a large cache AND a pipelined design
Idea: Cache hierarchy
CPU
Main
Memory
(DRAM)
RF
Level1
Cache
Level 2
Cache

## Slide 17: A Note on Manual vs. Automatic Management
2.6
Manual: Programmer manages data movement across levels
  -- too painful for programmers on substantial programs (volatile)
  “core” vs “off-chip” memory in the 50’s
  still done in some embedded processors (on-chip scratch pad SRAM in a cache)
Automatic: Hardware manages data movement across levels, transparently to the programmer
  ++ programmer’s life is easier
  the average programmer doesn’t need to know about it
    You don’t need to know how big the cache is and how it works to write a “correct” program! (What if you want a “fast” program?)

## Slide 18: Automatic Management in Memory Hierarchy
2.7
Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.
“By a slave memory I mean one which automatically accumulates to itself words that come from a slower main memory, and keeps them available for subsequent use without it being necessary for the penalty of main memory access to be incurred again.”

## Slide 19: Today’s Topic
00
01. The Problems in Memory
02. Locality and Cache
03. Memory Hierarchy
04. Cache Details
05. Performance Analysis

## Slide 20: A Modern Memory Hierarchy
3
20
Register File
32 words, sub-nsec
L1 cache
~32 KB, ~nsec
L2 cache
512 KB ~ 1MB, many nsec
L3 cache,
.....
Main memory (DRAM),
GB, ~100 nsec
Swap Disk
100 GB, ~10 msec
manual/compiler
register spilling
automatic
demand
paging
Automatic
HW cache
management
Memory
Abstraction

## Slide 21: Hierarchical Latency Analysis
3.1
For a given memory hierarchy level i it has a technology-intrinsic access time of ti, The perceived access time Ti is longer than ti
Except for the outer-most hierarchy, when looking for a given address there is
  a chance (hit-rate hi) you “hit” and access time is ti
  a chance (miss-rate mi) you “miss” and access time ti +Ti+1
  hi + mi = 1
Thus
Ti = hi·ti + mi·(ti + Ti+1)
Ti = ti + mi ·Ti+1
hi and mi are defined to be the hit-rate
and miss-rate of just the references that missed at Li-1
21

## Slide 22: Hierarchy Design Considerations
3.2
Recursive latency equation
Ti = ti + mi ·Ti+1
The goal: achieve desired T1 within allowed cost
Ti  ti is desirable
Keep mi low
  increasing capacity Ci lowers mi, but beware of increasing ti
  lower mi by smarter management (replacement::anticipate what you don’t need, prefetching::anticipate what you will need)
Keep Ti+1 low
  faster lower hierarchies, but beware of increasing cost
  introduce intermediate hierarchies as a compromise

## Slide 23: Intel Pentium 4 Example
3.3
90nm P4, 3.6 GHz
L1 D-cache
  C1 = 16K
  t1 = 4 cyc int / 9 cycle fp
L2 D-cache
  C2 =1024 KB
  t2 = 18 cyc int / 18 cyc fp
Main memory
  t3 = ~ 50ns or 180 cyc
Notice
  best case latency is not 1
  worst case access latencies are into 500+ cycles
if m1=0.1, m2=0.1
T1=7.6, T2=36
if m1=0.01, m2=0.01
T1=4.2, T2=19.8
if m1=0.05, m2=0.01
T1=5.00, T2=19.8
if m1=0.01, m2=0.50
T1=5.08, T2=108

## Slide 24: Intel Pentium 4 Example
3.3
90nm P4, 3.6 GHz
L1 D-cache
  C1 = 16K
  t1 = 4 cyc
L2 D-cache
  C2 =1024 KB
  t2 = 18 cyc
Main memory
  t3 = 180 cyc
Notice
  best case latency is not 1
  worst case access latencies are into 500+ cycles
if mL1=0.1, mL2=0.1
T1=7.6, T2=36, TM=180
if mL1=0.01, mL2=0.01
T1=?, T2=?, TM=180
if mL1=0.05, mL2=0.01
T1=?, T2=?, TM=180
if mL1=0.01, mL2=0.50
T1=?, T2=?, TM=180

## Slide 25: Intel Pentium 4 Example
3.3
if m1=0.1, m2=0.1
T1=7.6, T2=36, , TM=180
if m1=0.01, m2=0.01
T1=4.2, T2=19.8, , TM=180
if m1=0.05, m2=0.01
T1=5.00, T2=19.8, , TM=180
if m1=0.01, m2=0.50
T1=5.08, T2=108, , TM=180
90nm P4, 3.6 GHz
L1 D-cache
  C1 = 16K
  t1 = 4 cyc
L2 D-cache
  C2 =1024 KB
  t2 = 18 cyc
Main memory
  t3 = 180 cyc
Notice
  best case latency is not 1
  worst case access latencies are into 500+ cycles

## Slide 26: Today’s Topic
00
01. The Problems in Memory
02. Locality and Cache
03. Memory Hierarchy
04. Cache Details
05. Performance Analysis

## Slide 27: Cache
4
Generically, any structure that “memoizes” frequently used results to avoid repeating the long-latency operations required to reproduce the results from scratch, e.g. a web cache
Most commonly in the on-die context: an automatically-managed memory hierarchy based on SRAM
  memoize in SRAM the most frequently accessed DRAM memory locations to avoid repeatedly paying for the DRAM access latency

## Slide 28: Caching Basics
4.1
Block (line): Unit of storage in the cache
  Memory is logically divided into cache blocks that map to locations in the cache
When data referenced
  HIT: If in cache, use cached data instead of accessing memory
  MISS: If not in cache, bring block into cache
    Maybe have to kick something else out to do it
Some important cache design decisions
  Placement: where and how to place/find a block in cache?
  Replacement: what data to remove to make room in cache?
  Granularity of management: large, small, uniform blocks?
  Write policy: what do we do about writes?
  Instructions/data: Do we treat them separately?

## Slide 29: Cache Abstraction and Metrics
4.2
Cache hit rate = (# hits) / (# hits + # misses) = (# hits) / (# accesses)
Average memory access time (AMAT)
= ( hit-rate * hit-latency ) + ( miss-rate * miss-latency )
Aside: Can reducing AMAT improve performance?
Address
Tag Store
(is the address
in the cache?
+ bookkeeping)
Data Store
Hit/miss?
Data

## Slide 30: Blocks and Addressing the Cache
4.3
Memory is logically divided into fixed-size blocks
Each block maps to a location in the cache, determined by the index bits in the address
  used to index into the tag and data stores
Cache access:
  1) index into the tag and data stores with index bits in address
  2) check valid bit in tag store
  3) compare tag bits in address with the stored tag in tag store
If a block is in the cache, the stored tag should be valid and match the tag of the block
8-bit address
tag
index
byte in block
3 bits
3 bits
2b

## Slide 31: Direct-Mapped Cache: Placement and Access
4.4
Assume byte-addressable memory:
256 bytes, 8-byte blocks  32 blocks
Assume cache: 64 bytes, 8 blocks
  Direct-mapped: A block can go to only one location
  Addresses with same index contend for the same location
    Cause conflict misses
Tag store
Data store
Address
tag
index
byte in block
3 bits
3 bits
2b
V
tag
=?
MUX
byte in block
Hit?
Data

## Slide 32: Direct-Mapped Caches
4.4
Direct-mapped cache: Two blocks in memory that map to the same index in the cache cannot be present in the cache at the same time
  One index  one entry
Can lead to 0% hit rate if more than one block accessed in an interleaved manner map to the same index
  Assume addresses A and B have the same index bits but different tag bits
  A, B, A, B, A, B, A, B, …  conflict in the cache index
  All accesses are conflict misses

## Slide 33: Set Associativity
4.5
Addresses 0 and 8 always conflict in direct mapped cache
Instead of having one column of 8, have 2 columns of 4 blocks
Tag store
Data store
V
tag
=?
V
tag
=?
Address
tag
index
byte in block
3 bits
2 bits
3b
Logic
MUX
MUX
byte in block
SET
Hit?
Key idea: Associative memory within the set
+ Accommodates conflicts better (fewer conflict misses)
-- More complex, slower access, larger tag store

## Slide 34: Higher Associativity
4.6
4-way
+ Likelihood of conflict misses even lower
-- More tag comparators and wider data mux; larger tags
Tag store
Data store
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?

## Slide 35: Full Associativity
4.7
Fully associative cache
  A block can be placed in any cache location
Tag store
Data store
=?
=?
=?
=?
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?

## Slide 36: Associativity (and Tradeoffs)
4.8
Degree of associativity: How many blocks can map to the same index (or set)?
Higher associativity
  ++ Higher hit rate
  -- Slower cache access time (hit latency and data access latency)
  -- More expensive hardware (more comparators)
Diminishing returns from higher
  associativity
associativity
hit rate

## Slide 37: Issues in Set-Associative Caches
4.9
Think of each block in a set having a “priority”
  Indicating how important it is to keep the block in the cache
Key issue: How do you determine/adjust block priorities?
There are three key decisions in a set:
  Insertion, promotion, eviction (replacement)
Insertion: What happens to priorities on a cache fill?
  Where to insert the incoming block, whether or not to insert the block
Promotion: What happens to priorities on a cache hit?
  Whether and how to change block priority
Eviction/replacement: What happens to priorities on a cache miss?
  Which block to evict and how to adjust priorities

## Slide 38: Eviction/Replacement Policy
4.10
Which block in the set to replace on a cache miss?
  Any invalid block first
  If all are valid, consult the replacement policy
    Random
    FIFO
    Least recently used (how to implement?)
    Not most recently used
    Least frequently used?
    Least costly to re-fetch?
      Why would memory accesses have different cost?
    Hybrid replacement policies
    Optimal replacement policy? (depends on future access)

## Slide 39: Implementing LRU
4.11

## Slide 40: Implementing LRU
4.11
Idea: Evict the least recently accessed block
Problem: Need to keep track of access ordering of blocks
Question: 2-way set associative cache:
  What do you need to implement LRU perfectly?
Question: 4-way set associative cache:
  What do you need to implement LRU perfectly?
  How many different orderings possible for the 4 blocks in the set?
  How many bits needed to encode the LRU order of a block?
  What is the logic needed to determine the LRU victim?

## Slide 41: Approximations of LRU
4.12
Most modern processors do not implement “true LRU” (also called “perfect LRU”) in highly-associative caches
Why?
  True LRU is complex
  LRU is an approximation to predict locality anyway (i.e., not the best possible cache management policy)
Examples:
  Not MRU (not most recently used)
  Hierarchical LRU: divide the 4-way set into 2-way “groups”, track the MRU group and the MRU way in each group

## Slide 42: What’s In A Tag Store Entry?
4.13
Valid bit
Tag
Replacement policy bits
Dirty bit?
  Write back vs. write through caches

## Slide 43: Handling Writes
4.14
  When do we write the modified data in a cache to the next level?
    Write through: At the time the write happens
    Write back: When the block is evicted
  Write-back
    + Can consolidate multiple writes to the same block before eviction
      Potentially saves bandwidth between cache levels + saves energy
  -- Need a bit in the tag store indicating the block is “dirty/modified”
  Write-through
    + Simpler
    + All levels are up to date. Consistency: Simpler cache coherence because no need to check lower-level caches
    -- More bandwidth intensive; no coalescing of writes

## Slide 44: Handling Writes (II)
4.14
Do we allocate a cache block on a write miss?
  Allocate on write miss: Yes
  No-allocate on write miss: No
Allocate on write miss
  + Can consolidate writes instead of writing each of them individually to next level
  + Simpler because write misses can be treated the same way as read misses
  -- Requires (?) transfer of the whole cache block
No-allocate
  + Conserves cache space if locality of writes is low (potentially better cache hit rate)

## Slide 45: Handling Writes (III)
4.14
What if the processor writes to an entire block over a small amount of time?
Is there any need to bring the block into the cache from memory in the first place?
Ditto for a portion of the block, i.e., subblock
  E.g., 4 bytes out of 64 bytes

## Slide 46: Instruction vs. Data Caches
4.15
Separate or Unified?
Unified:
  + Dynamic sharing of cache space: no overprovisioning that might happen with static partitioning (i.e., split I and D caches)
  -- Instructions and data can thrash each other (i.e., no guaranteed space for either)
  -- I and D are accessed in different places in the pipeline. Where do we place the unified cache for fast access?
First level caches are almost always split
  Mainly for the last reason above
Second and higher levels are almost always unified

## Slide 47: Multi-level Caching in a Pipelined Design
4.16
First-level caches (instruction and data)
  Decisions very much affected by cycle time
  Small, lower associativity
  Tag store and data store accessed in parallel (why?)
Second-level caches
  Decisions need to balance hit rate and access latency
  Usually large and highly associative; latency not as important
  Tag store and data store accessed serially (why?)
Serial vs. Parallel access of levels
  Serial: Second level cache accessed only if first-level misses
  Second level does not see the same accesses as the first
    First level acts as a filter (filters some temporal and spatial locality)
    Management policies are therefore different

## Slide 48: Today’s Topic
00
01. The Problems in Memory
02. Locality and Cache
03. Memory Hierarchy
04. Cache Details
05. Performance Analysis

## Slide 49: Cache Parameters vs. Miss/Hit Rate
5
Cache size
Block size
Associativity
Replacement policy
Insertion/Placement policy

## Slide 50: Cache Parameters vs. Miss/Hit Rate
5
Cache size
Block size
Associativity

## Slide 51: Cache Size
5.1
Cache size: total data (not including tag) capacity
  bigger can exploit temporal locality better
  not ALWAYS better
Too large a cache adversely affects hit and miss latency
  smaller is faster => bigger is slower
  access time may degrade critical path
Too small a cache
  doesn’t exploit temporal locality well
  useful data replaced often
Working set: the whole set of data the executing application references
  Within a time interval
hit rate
cache size
“working set”
size

## Slide 52: Block Size
5.2
Block size is the data that is associated with an address tag
  not necessarily the unit of transfer between hierarchies
    Sub-blocking: A block divided into multiple pieces (each with V bit)
      Can improve “write” performance
Too small blocks
  don’t exploit spatial locality well
  have larger tag overhead
Too large blocks
  too few total # of blocks  less
    temporal locality exploitation
  waste of cache space and bandwidth/energy
  if spatial locality is not high
52
hit rate
block
size

## Slide 53: Large Blocks: Critical-Word and Subblocking
5.3
Large cache blocks can take a long time to fill into the cache
  fill cache line critical word first
  restart cache access before complete fill
Large cache blocks can waste bus bandwidth
  divide a block into subblocks
  associate separate valid bits for each subblock
  When is this useful?
tag
subblock
v
subblock
v
subblock
v
d
d
d

## Slide 54: Associativity
5.4
How many blocks can map to the same index (or set)?
Larger associativity
  lower miss rate, less variation among programs
  diminishing returns, higher hit latency
Smaller associativity
  lower cost
  lower hit latency
    Especially important for L1 caches
Power of 2 associativity required?
54
associativity
hit rate

## Slide 55: Classification of Cache Misses
5.5
Compulsory miss
  first reference to an address (block) always results in a miss
  subsequent references should hit unless the cache block is displaced for the reasons below
Capacity miss
  cache is too small to hold everything needed
  defined as the misses that would occur even in a fully-associative cache (with optimal replacement) of the same capacity
Conflict miss
  defined as any miss that is neither a compulsory nor a capacity miss

## Slide 56: How to Reduce Each Miss Type
5.6
Compulsory
  Caching cannot help
  Prefetching
Conflict
  More associativity
  Other ways to get more associativity without making the cache associative
    Victim cache
    Hashing
    Software hints?
Capacity
  Utilize cache space better: keep blocks that will be referenced
  Software management: divide working set such that each “phase” fits in cache

## Slide 57: Improving Basic Cache Performance
5.7
Reducing miss rate
  More associativity
  Alternatives/enhancements to associativity
    Victim caches, hashing, pseudo-associativity, skewed associativity
  Better replacement/insertion policies
  Software approaches
Reducing miss latency/cost
  Multi-level caches
  Critical word first
  Subblocking/sectoring
  Better replacement/insertion policies
  Non-blocking caches (multiple cache misses in parallel)
  Multiple accesses per cycle
  Software approaches