## Slide 1
Computer Organization and Architecture
Lecture6 MIPS ISA
Jihe Wang
wangjihe@nwpu.edu.cn

## Slide 2
Today's
Topic
01. Register and Memory Orgnaztion of MIPS
02. Typical Instructions
03. Machine Language
00
Today's Topics
04. Programming with MIPS instructions

## Slide 3
1.1
Register Orgnzation
32 general purpose registers:r0-r31
A 64-bit Register for Multiply and divide
A 32-bit Register for the program address
PC

## Slide 4
1.1
Memory Orgnaztion
Stack
Dynamic data (heap)
Static data (globals)
Text (instructions)
The space allocated on stack by a procedure is termed the activation
record (includes saved values and data local to the procedure) – frame
pointer points to the start of the record and stack pointer points to the
end – variable addresses are specified relative to $fp as $sp may
change during the execution of the procedure
$gp points to area in memory that saves global variables
Dynamically allocated storage (with malloc()) is placed on the heap
//main.cpp int a = 0; //global initialized area char *p1; //global uninitialized area main() { int b; //stack char s[] = “abc”; //stack char *p2; //stack char *p3 = “123456”; // 123456 in static, p3 in stack static int c =0； globle initialized area p1 = (char *)malloc(10); p2 = (char *)malloc(20); // allocated spaces are in heap strcpy(p1, “123456”); //123456 in static, compiler could use a same place with p3. }

## Slide 5
1.2
Instruction Format
OPCOD
OPERAND
OPERAND
…
The OPCOD defines the operation of the instruction, such as addition, subtraction, data transfer, etc.
The OPERANDs designate the operate object of the OPCOD, which are the index of the register file, the address of memory, etc.
Both the OPCOD and OPERAND are represented in binary.

## Slide 6
Arithmetic Instructions
Logical Instructions
Load/Store Instructions
Comparison Instructions
Branch Instructions
Jump Instructions
Other Instructions
2
Typical Instructions of MIPS

## Slide 7
2.1
Arithmetic Instructions
add rd, rs, rt
addu rd, rs, rt
addi rd, rs, imm
addiu rd, rs, imm
sub rd, rs, rt
subu rd, rs, rt
mult rs, rt
multu rs, rt
mul rd, rs, rt #put the low-order 32 bits of the product into the register rd
div rs, rt
divu rs, rt
mfhi rd #rd<-hi
mflo rd #rd<-lo
mthi rs #hi<-rs
mtlo rs #lo<-rs

## Slide 8
madd rs,rt #(Hi,Lo)<-(rs X rt)+(Hi,Lo)
maddu rs,rt #(Hi,Lo)<-(rs X rt)+(Hi,Lo)
msub rs, rt#(Hi,Lo)<-(rs X rt)-(Hi,Lo)
msubu rs, rt#(Hi,Lo)<-(rs X rt)-(Hi,Lo)
clo rd,rs
clz rd,rs
2.1
Arithmetic Instructions -Continued
#Count the number of leading ones (zeros) in the word in the register rs and put the result into register rd. If a word is all ones (zeros), the result is 32

## Slide 9
2.2
Logical Instructions
and rd, rs, rt
andi rt, rs, imm
or rd, rs, rt
ori rt, rs, imm
xor rd, rs, rt
xori rt, rs, imm
nor rd, rs, rt
sll rd, rt, shamt
sllv rd, rt, rs
sra rd, rt, shamt
srav rd, rt, rs
srl rd, rt, shamt
srlv rd, rt, rs
right
Logical
arithmetic
left

## Slide 10
2.3
Load/Store Instructions
lui rt,imm
lh rt, address
lhu rt, address
lw rt, address
lwc1 ft, address
lwl rt, address
lwr rt, address
ll rt, address
sb rt, address (byte)
sh rt, address (half word)
sw rt, address
swc1 ft, address (Coprocessor 1)
sdc1 ft, address
swl rt, address
swr rt, address
sc rt, address
Load Linked
Store Conditional
double

## Slide 11
2.3
Load/Store Instructions: lwl $t0, vAddr
$t0
pointer
“X And 0” to set 0;
“X or 0” to keep X;
“X And 1” to keep X;
“X or 1” to set 1;

## Slide 12
2.4
Comparison Instructions
slt rd, rs, rt
sltu rd, rs, rt
slti rt, rs, imm
sltiu rt, rs, imm
#Set rd if rs less than rt, otherwise clear rd
#Set rt if rs less than imm, otherwise clear rt

## Slide 13
2.5
Branch Instructions
beq rs, rt, label
bne rs, rt, label
bgez rs, label
bgtz rs, label
blez rs, label
bltz rs, label
bgezal rs, label #in addition to conditional branch,
bltzal rs,label #store the PC into $ra (r31)
Notes: To test a GPR then do a PC-relative conditional procedure call.

## Slide 14
2.6
Jump Instructions
j target
jr rs #jump to the instruction whose address is
# in register rs
jal target #in addition to jump, store the PC to
# $ra (r31), subroutine call
jalr rs #jump to the instruction whose #address is in rs, save pc in ra(which defaults to 31)

## Slide 15
PC
4
26
32
00
from the low order 26 bits of the jump instruction
op
6
target
3.3
Machine Language-Jump Instruction(J-Format)
J target
How about Jr instruction ?
Notes: If-then-else code compilation

## Slide 16
2.7
Other Instructions

## Slide 17
2.8
Psuedo-instructions
abs rdest, rsrc
div rdest, rsrc1, rsrc2
divu rdest, rsrc1, rsrc2
mulo rdest, rsrc1, rsrc2
mulo rdest, rsrc1, rsrc2
neg rdest, rsrc
negu rdest, rsrc
not rdest, rsrc
rem rdest, rsrc1, rsrc2
remu rdest, rsrc1, rsrc2
rol rdest, rsrc1, rsrc2
ror rdest, rsrc1, rsrc2
li rdest, imm
sd rsrc, address
ush rsrc, address
usw rsrc, address
b label
beqz rsrc, label
bge rsrc1, rsrc2, label
bgeu rsrc1, rsrc2, label
bgt rsrc1, rsrc2, label
bgtu rsrc1, rsrc2, label
ble rsrc1, rsrc2, label
bleu rsrc1, rsrc2, label
blt rsrc1, rsrc2, label
bltu rsrc1, rsrc2, label
bnez rsrc. label

## Slide 18
3
Machine Language-Instruction Format
5
5
5
6
5
6

## Slide 19
Instructions, like registers and words of data, are 32 bits long
Arithmetic Instruction Format (R format):
op rs rt rd shamt funct
op 6-bits opcode that specifies the operation
rs 5-bits register file address of the first source operand
rt 5-bits register file address of the second source operand
rd 5-bits register file address of the result’s destination
shamt 5-bits shift amount (for shift instructions)
funct 6-bits function code augmenting the opcodeadd
5
5
5
6
add
$t0
$s1
$S2
3.1
Machine Language-Add Instruction(R-Format)
“add” can be replaced by other operations, such as sub, and, sllv, et. al.
5
6

## Slide 20
What patterns do you see? Why are they there?
[MIPS R4000 Microprocessor User’s Manual]
3.1
R-Type Encoding

## Slide 21
Load/Store Instruction Format (I format):
op rs rt 16 bit offset
Memory
data
word address (hex)
0x00000000
0x00000004
0x00000008
0x0000000c
0xf f f f f f f f
$s2
0x12004094
2410 + $s2 =
0x120040ac
0x120040ac
$t0
lw
$t0
24
$s2
“lw” can be replaced by other operations, such as st, bnz, ori, et. al.
3.2
Machine Language-Add Instruction(I-Format)
Notes: destination address no longer in the rd field - now in the rt field
offset limited to 16 bits - so can’t get to every location in memory (with a fixed base address)

## Slide 22
[MIPS R4000 Microprocessor User’s Manual]
3.2
Reg-Immed Instruction Encoding

## Slide 23
op rs rt rd funct
Register
word operand
base register
op rs rt offset
Memory
word or byte operand
op rs rt operand
Register addressing – operand is in a register
Base (displacement) addressing – operand is at the memory location whose address is the sum of a register and a 16-bit constant contained within the instruction
    Register relative (indirect) with 0($a0)
    Pseudo-direct with addr($zero)
Immediate addressing – operand is a 16-bit constant contained within the instruction
3.4
MIPS Operand Addressing Modes
<<2

## Slide 24
PC-relative addressing –instruction address is the sum of the PC and a 16-bit constant contained within the instruction
Pseudo-direct addressing – instruction address is the 26-bit constant contained within the instruction concatenated with the upper 4 bits of the PC
op rs rt offset
Program Counter (PC)
Memory
branch destination instruction
op jump address
Program Counter (PC)
Memory
jump destination instruction
|
|
3.5
MIPS Instruction Addressing Modes
<<2
<<2

## Slide 25
Arithmetic and logical operation
  Use the corresponding arithmetic/logical instruction directly, if all the operands are in the registers (source operand can be immediate data).
  If the source operand is located in memory, it should be moved into register by ‘lw’ before computing.
  If the destination operand is a memory operand, it should be transferred to memory use ‘sw’ instruction after computing.
  Some examples…
4
Programming with MIPS Instruction

## Slide 26
4
Programming with MIPS Instruction
if (i==j)
f=g+h;
else
f=f-h;
Suppose the 5 variables are in the register as follows:
i:$s0, j:$s1, f:$s2, g: $s3, h:$s4

## Slide 27
4
Programming with MIPS Instruction
for (i=1000; i>=0;i--)
A[i]=A[i]+s;
Assumption:
The address of i: $s0;
address of A[0]:4
s:$s1;
Loop:
lw $s2, 4($s0)
add $s2, $s2, $s1
sw $s2, 4($s0)
subi $s0, $s0,4
bnez $s0, Loop

## Slide 28
4
Programming-Procedure Call
Stack can be used to store and restore the context of the procedure call.

## Slide 29
4
Programming-Stack
Located in Memory
Implementation
  Was supported by ISA, specified instructions, such as push and pop instructions in 80X86
  By software, such as in MIPS. $sp, which stores the address of top of the stack, should be updated by the programmer.

## Slide 30
4
Programming-Procedure Call
Put the parameters in a place where the procedure can access them.
Transfer control to the procedure.
Acquire the storage resources needed for the procedure.
Perform the desired task.
Put the result value in a place where the calling program can access it.
Return the control to the point of origin, since a procedure can be called from several points in a program.

## Slide 31
4
Programming-Register conventions

## Slide 32
4
Programming-MIPS/GCC procedure call conventions
The first 4 parameters are transferred via register.

## Slide 33
4
Programming- C example: swap
Assumption:
Swap can be called as a procedure
temp: $15
Parameters are stored in $a1 and $a2
$16 is used as scratch reg

## Slide 34
4
Programming- MIPS: swap