## Slide 1: Lecture5 More ISA
Computer Organization and Architecture
Jihe Wang
wangjihe@nwpu.edu.cn

## Slide 2: Outline
Functional Design of Instruction Set
  a.k.a. ISA Basic (2.1~2.5)
More ISA (Instruction Set Principles)
  Detailed ISA, Endian-ness, Addressing, (Today’s Topic), CISC vs RISC
More Detailed MIPS ISA
    Types of MIPS ISA, Procedure call, Programming with MIPS Assembly
0.0

## Slide 3: ISA Principles
Classifying ISA
Memory Addressing
Instruction Format
Operations in the Instruction Set
0.0

## Slide 4: Classifying ISA
4 types of Instruction Sets (Internal Storage of Processors)
  Stack
  Accumulator
  Register-memory
  Register-register
1.0
Notes: The arrows indicate whether the oper- and is an input or the result of the ALU operation, or both an input and result. Lighter shades indicate inputs, and the dark shade indicates the result. In (a), a Top Of Stack register (TOS), points to the top input operand, which is com- bined with the operand below. The first operand is removed from the stack, the result takes the place of the second operand, and TOS is updated to point to the result. All operands are implicit. In (b), the Accumulator is both an implicit input operand and a result. In (c), one input operand is a register, one is in memory, and the result goes to a register. All operands are registers in (d) and, like the stack architecture, can be transferred to memory only via sepa- rate instructions: push or pop for (a) and load or store for (d).

## Slide 5: Classifying ISA
4 types of Instruction Sets (Internal Storage of Processors)
  Stack
  Accumulator
  Register- memory
  Register-register memory
2.1
Notes: The arrows indicate whether the operand is an input or the result of the ALU operation, or both an input and result. Lighter shades indicate inputs, and the dark shade indicates the result. In (a), a Top Of Stack register (TOS), points to the top input operand, which is combined with the operand below. The first operand is removed from the stack, the result takes the place of the second operand, and TOS is updated to point to the result. All operands are implicit. In (b), the Accumulator is both an implicit input operand and a result. In (c), one input operand is a register, one is in memory, and the result goes to a register. All operands are registers in (d) and, like the stack architecture, can be transferred to memory only via separate instructions: push or pop for (a) and load or store for (d). As the figures show, there are really two classes of register computers. One class can access memory as part of any instruction, called register-memory archi- tecture, and the other can access memory only with load and store instructions, called load-store architecture.

## Slide 6: Example
C=A+B
  All variables are stored in memory
Stack | Accumulator | Register (register-memory) | Register (load-store)
Push A | Load A | Load R1, A | Load R1, A
Push B | Add B | Add R3, R1, B | Load R2, B
Add | Store | Store R3, C | Add R3, R1, R2
Pop C |  |  | Store R3,C
Compare: Instruction length (bit size), Instruction #, and Instruction Execution Time
With implicit operands
Notes: he code sequence for C = A + B for four classes of instruction sets. Note that the Add instruction has implicit operands for stack and accumulator architectures, and explicit operands for register architectures. It is assumed that A, B, and C all belong in memory (address) and that the values of A and B cannot be destroyed. This table shows the Add operation for each class of architecture. Obviously, the implicit operands are simplifying instructions, and the bit size reduces respectively. However, the dependency between memory accessing and ALU operations leads to a long ALU instruction latency for those with explicit memory address operands.

## Slide 7: Register Architecture Benefits
General-purpose Register (GPR)!
Every new architecture designed after 1980 uses a load-store register architecture.
  registers are faster than memory (like other forms of internal storage)
  Registers are more efficient for a compiler to use than other forms of internal storage
    (A*B) – (B*C) – (A*D) may do * in any order (vs. stack)
  Registers can be used to hold variables
    The memory traffic reduces, the program speeds up
    the code density improves
Notes: For the compiling efficiency of Register Architecture, for example, on a register computer the expression (A*B) – (B*C) – (A*D) may be evaluated by doing the multiplications in any order, which may be more efficient because of the location of the operands or because of pipelining concerns (see P.H. Chapter 3). Nevertheless, on a stack computer the hardware must evaluate the expression in only one order, since operands are hidden on the stack, and it may have to load an operand multiple times.
More importantly, registers can be used to hold variables. When variables are allocated to registers, the memory traffic reduces, the program speeds up (since registers are faster than memory), and the code density improves (since a register can be named with fewer bits than can a memory location).

## Slide 8: Examples: Memory Operands per ALU Instruction
Number of memory addresses | Maximum number of operands allowed | Type of architecture | Examples
0 | 3 | Load-store | Alpha, ARM, MIPS, PowerPC, SPARC, SuperH, TM32
1 | 2 | Register-memory | IBM 360/370, Intel 80x86, Motorola 68000, TI TMS320C54x
2 | 2 | Memory-memory | VAX (also has two-operand formats)
3 | 3 | Memory-memory | VAX (also has three-operand formats)
Notes: This slide shows the typical combinations of memory operands and total operands per typical ALU instruction with examples of computers. Computers with no memory reference per ALU instruction are called load-store or register- register computers. Instructions with multiple memory operands per typical ALU instruction are called register-memory or memory-memory, according to whether they have one or more than one memory operand.

## Slide 9: Memory Operands Trade-off I
Register-register : 0 mem operand / typical ALU instruction, 3 operands / typical ALU instruction (0, 3)
  Simple, fixed-length instruction encoding
  Simple code generation model
  Similar # of clocks to execute
  Higher instruction # than architectures with memory references in instructions
  Lower instruction density leads to larger programs
Notes: Advantages and disadvantages of the three most common types of general-purpose register computers. The notation (m, n) means m memory operands and n total operands. In general, computers with fewer alternatives simplify the compiler’s task since there are fewer decisions for the compiler to make (H.P. Appendix A.8). Computers with a wide variety of flexible instruction formats reduce the number of bits required to encode the program. The number of registers also affects the instruction size since you need log2 (number of registers) for each register specifier in an instruction. Thus, doubling the number of registers takes 3 extra bits for a register-register architecture, or about 10% of a 32-bit instruction.

## Slide 10: Memory Operands Trade-off II
Register-memory: (1, 2)
  Data can be accessed without a separate pre load instruction
  Instruction format tends to be easy to encode
  Good Instruction density
  Operands are not equivalent since a source operand in a binary operation is destroyed
  Encoding a register number and a memory address in each instruction may restrict the number of registers
  Clocks per instruction vary by operand location
Notes: These comparisons are based on the table of last slide. Binary operation means Add $s1, A, in which the operand in $s1 is modified with the sum.

## Slide 11: Memory Operands Trade-off III
Memory-memory: (2, 2) or (3, 3)
  Most compact. Doesn’t waste registers for temporaries.
  Large variation in instruction size, especially for three-operand instructions.
  Large variation in work per instruction.
  Memory accesses create memory bottleneck
Not used today
Notes: Here through Section 4.0 we summarize those characteristics we would expect to find in a new instruction set architecture, building the foundation for the MIPS architecture introduced in next lecture. From this section we should clearly expect the use of general-purpose registers. This section combined with pipelining lecture, leads to the expectation of a load-store version of a general-purpose register architecture. With the class of architecture covered, the next slide is addressing operands.

## Slide 12: Memory Addressing
How to access the source operand and store the result?
  Where can we put the source operand and the result?
    Memory, registers, etc
How can we access the data in memory?
Which operand can/cannot be stored in memory?
2.0
OPCOD
OPERAND
OPERAND
…

## Slide 13: Where to Store Data
Memory
Registers
Stack*
IO Interface
CPU
I/O
Memory
Program
(Instructions)
Notes: There are two serials of hardware support to implement stack function:
Stack in main memory and Stack in registers or dedicated memory (also called stack-based machine)
The x87 floating point architecture is an example of a set of registers organized as a stack where direct access to individual registers (relative the current top) is also possible. As with stack-based machines in general, having the top-of-stack as an implicit argument allows for a small machine code footprint with a good usage of bus bandwidth and code caches, but it also prevents some types of optimizations possible on processors permitting random access to the register file for all (two or three) operands. A stack structure also makes superscalar implementations with register renaming (for speculative execution) somewhat more complex to implement, although it is still feasible, as exemplified by modern x87 implementations.
Sun SPARC, AMD Am29000, and Intel i960 are all examples of architectures using register windows within a register-stack as another strategy to avoid the use of slow main memory for function arguments and return values.
There are also a number of small microprocessors that implements a stack directly in hardware and some microcontrollers have a fixed-depth stack that is not directly accessible. Examples are the PIC microcontrollers, the Computer Cowboys MuP21, the Harris RTX line, and the Novix NC4016. Many stack-based microprocessors were used to implement the programming language Forth at the microcode level. Stacks were also used as a basis of a number of mainframes and mini computers. Such machines were called stack machines, the most famous being the Burroughs B5000.
Anyhow, the stack-based machine is more like an alternative. The main stream system, now, support software stack which is mapped in memory.

## Slide 14: Registers
Located in CPU, So can be accessed very fast! (Registers can be located anywhere in digital system)
The amount is usually small.
The data should be swapped to memory if the amount of variables exceeds that of registers.
Specified with the index in the instruction
  5 bits in MIPS
Notes: Although Intel instructions vary in size from one byte up to fourteen bytes, all Intel instructions have the same six-part structure. Understanding the purpose of each part is the first step to learning the sizes of the different Intel instructions. The parts of an Intel-format instruction are listed below, in the order that they appear in the instruction:
Prefixes: 0-4 bytes
Opcode: 1-2 bytes
ModR/M: 1 byte
SIB: 1 byte
Displacement: 1 byte or word
Immediate: 1 byte or word
If the instruction requires it, the ModR/M byte comes after the opcode. This byte tells the processor which registers or memory locations to use as the instruction's operands. The byte has the following structure:
6 5 3 2 0
mod reg2 reg1
Both the reg1 and reg2 fields take three-bit register codes, indicating which registers to use as the instruction's operands. By default, reg1 is the source operand and reg2 is the destination. Some opcodes, such as the OR opcode mentioned above, contain a direction bit which overrides this default. Other instructions require a single operand. If an instruction requires only one operand, the unused reg2 field holds extra opcode bits rather than a register code.

## Slide 15: Memory
Often implemented with DRAM. (May be implemented with NVM in the future)
Often organized in flat logically. Accessed with the address of every data(0~FFFFFFFFH)
A huge amount of capacity
Interact with CPU via memory bus
Physical Address VS Logical Address in programming!
0
1
2
FFFFFFFFH

## Slide 16: Addressing Objects: Endianness and Alignment
Big Endian: address of most significant byte = word address (xx00 = Big End of word)
  IBM 360/370, Motorola 68k, MIPS, Sparc, HP PA
Little Endian: address of least significant byte = word address (xx00 = Little End of word)
  Intel 80x86, DEC Vax, DEC Alpha (Windows NT)
msb
lsb
3 2 1 0
little endian byte 0
0 1 2 3
big endian byte 0
Alignment: require that objects fall on address that is multiple of their size.
0 1 2 3
Aligned
Not
Aligned
Endian War
Notes: Actually, the Endian war is shown as the different answer of “How is a memory address interpreted? That is, what object is accessed as a function of the address and the length?”
There are two different conventions for ordering the bytes within a larger object.
Little Endian byte order puts the byte whose address is “x . . . x000” at the least-significant position in the double word (the little end).
Big Endian byte order puts the byte whose address is “x . . . x000” at the most- significant position in the double word (the big end).

## Slide 17: Top 10 80x86 Instructions

## Slide 18: Operation Summary
Support these simple instructions, since they will dominate the number of instructions executed:
  load,
  store,
  add,
  subtract,
  move register-register,
  and,
  shift,
  compare equal, compare not equal,
  branch, jump,
  call,
  return;

## Slide 19: Appendix: Data Types
Bit: 0, 1
Bit String: sequence of bits of a particular length
4 bits is a nibble
8 bits is a byte
16 bits is a half-word
32 bits is a word
64 bits is a double-word
Character:
ASCII 7 bit code
UNICODE 16 bit code
Decimal:
digits 0-9 encoded as 0000b thru 1001b
two decimal digits packed per 8 bit byte
Integers:
2's Complement
Floating Point:
Single Precision
Double Precision
Extended Precision
M x R
E
How many +/- #'s?
Where is decimal pt?
How are +/- exponents
represented?
exponent
base
mantissa

## Slide 20: Next Lecture
Detailed MIPS ISA
Reading Assignment
  P.H. Chapter 2
  H.P. Appendix A (5th Edition)