## Slide 1
Computer Organization and Architecture
Lecture12 Datapath Design -- Multi-Cycle
Jihe Wang
wangjihe@nwpu.edu.cn

## Slide 2: Today’s Topic
00
01. Introduction & Recap
02. Analyze the Single Cycle Microprocessor
03. Construct a Multi-Cycle Datapath
04. More details of the Multi-Cycle Datapath
05. Control
06. Exceptions
07. Summary

## Slide 3: Where are we now?
1
The Five Classic Components of a Computer
Today's Topic: Design a Mulyi-Cycle Processor
Control
Datapath
Memory
Processor
Input
Output

## Slide 4: Recap: Processor Design is a Process
1.1
Bottom-up
  assemble components in target technology to establish critical timing
Top-down
  specify component behavior from high-level requirements
Iterative refinement
  establish partial solution, expand and improve
datapath
control
processor
Instruction Set
Architecture

Reg. File
Mux
ALU
Reg
Mem
Decoder
Sequencer
Cells
Gates

## Slide 5: Recap: A Single Cycle Datapath
1.2
32
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst
Extender
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
Mux
MemtoReg
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr
ALU
Instruction
Fetch Unit
Clk
Equal
Instruction<31:0>
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rs
Rt
nPC_sel

## Slide 6: Recap: The “Truth Table” for the Main Control
1.3
R-type
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
Branch
Jump
ExtOp
ALUop (Symbolic)
1
0
0
1
0
0
0
x
“R-type”
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Add
x
1
x
0
1
0
0
1
Add
x
0
x
0
0
1
0
x
Subtract
x
x
x
0
0
0
1
x
xxx
op
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
ALUop <2>
1
0
0
0
0
x
ALUop <1>
0
1
0
0
0
x
ALUop <0>
0
0
0
0
1
x
Main
Control
op
6
ALU
Control
(Local)
func
3
6
ALUop
ALUctr
3
RegDst
ALUSrc
:
Notes: Now that we have taken care of the Local Control (ALU Control), let’s refocus our attention to the Main Controller.
The job of the Main Control is to look at the Opcode field of the instruction and generate these control signals for the datapath (RegDst, ... ExtOp) as well as the 3-bit ALUop field for the ALU Control.
Here, I have shown you the symbolic value of the ALUop field as well as the actual bit assignment.
For example here (2nd column), the R-type ALUop is encode as 100 and the Add operation (3rd column) is encoded as 000..
This is call a quote “Truth Table” unquote because if you think about it, this is like having the truth table rotates 90 degrees.
Let me show you what I mean by that.
+3 = 65 min. (Y:45)

## Slide 7: Recap: PLA Implementation of the Main Control
1.4
op<0>
op<5>
.
.
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
R-type
ori
lw
sw
beq
jump
RegWrite
ALUSrc
MemtoReg
MemWrite
Branch
Jump
RegDst
ExtOp
ALUop<2>
ALUop<1>
ALUop<0>
Notes: Similarly, for ALUSrc, we need to OR the ori, load, and store terms together because we need to assert the ALUSrc signals whenever we have the Ori, load, or store instructions.
The RegDst, MemtoReg, MemWrite, Branch, and Jump signals are very simple. They don’t need to OR any product terms together because each is asserted for only one instruction.
For example, RegDst is asserted ONLY for R-type instruction and MemtoReg is asserted ONLY for load instruction.
ExtOp, on the other hand, needs to be set to 1 for both the load and store instructions so the immediate field is sign extended properly.
Therefore, we need to OR the load and store terms together to form the signal ExtOp.
Finally, we have the ALUop signals.
But clever encoding of the ALUop field, we are able to keep them simple so that no OR gates is needed.
If you don’t already know, this regular structure with an array of AND gates followed by another array of OR gates is called a Programmable Logic Array, or PLA for short.
It is one of the most common ways to implement logic function and there are a lot of CAD tools available to simplify them.
+3 = 70 min. (Y:50)

## Slide 8: Recap: Systematic Generation of Control
1.5
In our single-cycle processor, each instruction is realized by exactly one control command or “microinstruction”
  in general, the controller is a finite state machine
  microinstruction can also control sequencing (see later)
Control Logic / Store
(PLA, ROM)
OPcode
Datapath
Instruction
Decode
Conditions
Control
Points
microinstruction

## Slide 9: The Big Picture: Where are We Now?
1.6
The Five Classic Components of a Computer
Today’s Topic: Designing the Datapath for the Multiple Clock Cycle Datapath
Control
Datapath
Memory
Processor
Input
Output

## Slide 10: Today’s Topic
00
01. Introduction & Recap
02. Analyze the Single Cycle Microprocessor
03. Construct a Multi-Cycle Datapath
04. More details of the Multi-Cycle Datapath
05. Control
06. Exceptions
07. Summary

## Slide 11: Abstract View of our single cycle processor
2.1
x = 1011000
looks like a FSM with PC as state
PC
Next PC
Register
Fetch
ALU
Reg.
Wrt
Mem
Access
Data
Mem
Instruction
Fetch
Result Store
ALUctr
RegDst
ALUSrc
ExtOp
MemWr
Equal
nPC_sel
RegWr
MemWr
MemRd
Main
Control
ALU
control
op
fun
Ext

## Slide 12: What’s wrong with our CPI=1 processor?
2.2
Long Cycle Time
All instructions take as much time as the slowest
Real memory is not as nice as our idealized memory
  cannot always get the job done in one (short) cycle
PC
Inst Memory
mux
ALU
Data Mem
mux
PC
Reg File
Inst Memory
mux
ALU
mux
PC
Inst Memory
mux
ALU
Data Mem
PC
Inst Memory
cmp
mux
Reg File
Reg File
Reg File
Arithmetic & Logical
Load
Store
Branch
Critical Path
setup
setup

## Slide 13: Memory Access Time
2.3
Physics => fast memories are small (large memories are slow)
  question: register file vs. memory
=> Use a hierarchy of memories
Storage Array
selected word line
address
storage cell
bit line
sense amps
address
decoder
Cache
Processor
1 time-period
proc. bus
L2
Cache
mem. bus
2-3 time-periods
20 - 50 time-periods
memory

## Slide 14: Reducing Cycle Time
2.4
Cut combinational dependency graph and insert register / latch
Do same work in two fast cycles, rather than one slow one
May be able to short-circuit path and remove some components for some instructions!
storage element
Acyclic
Combinational
Logic
storage element
storage element
Acyclic
Combinational
Logic (A)
storage element
storage element
Acyclic
Combinational
Logic (B)


## Slide 15: Today’s Topic
00
01. Introduction & Recap
02. Analyze the Single Cycle Microprocessor
03. Construct a Multi-Cycle Datapath
04. More details of the Multi-Cycle Datapath
05. Control
06. Exceptions
07. Summary

## Slide 16: Basic Limits on Cycle Time
3.1
Next address logic
  PC <= branch ? PC + offset : PC + 4
Instruction Fetch
  InstructionReg <= Mem[PC]
Register Access
  A <= R[rs]
ALU operation
  R <= A + B
PC
Next PC
Operand
Fetch
Exec
Reg.
File
Mem
Access
Data
Mem
Instruction
Fetch
Result Store
ALUctr
RegDst
ALUSrc
ExtOp
MemWr
nPC_sel
RegWr
MemWr
MemRd
Control

## Slide 17: Partitioning the CPI=1 Datapath
3.2
Add registers between smallest steps
Place enables on all registers
PC
Next PC
Operand
Fetch
Exec
Reg.
File
Mem
Access
Data
Mem
Instruction
Fetch
Result Store
ALUctr
RegDst
ALUSrc
ExtOp
MemWr
nPC_sel
RegWr
MemWr
MemRd
Equal

## Slide 18: Example Multicycle Datapath
3.3
Critical Path ?
PC
Next PC
Operand
Fetch
Instruction
Fetch
nPC_sel
IR
Reg
File
Ext
ALU
Reg.
File
Mem
Access
Data
Mem
Result Store
RegDst
RegWr
MemWr
MemRd
S
M
MemToReg
Equal
ALUctr
ALUSrc
ExtOp
A
B
E

## Slide 19: Example Multicycle Datapath
3.3
Critical Path ?
PC
Next PC
Operand
Fetch
Instruction
Fetch
nPC_sel
IR
Reg
File
Ext
ALU
Reg.
File
Mem
Access
Data
Mem
Result Store
RegDst
RegWr
MemWr
MemRd
S
M
MemToReg
Equal
ALUctr
ALUSrc
ExtOp
A
B
E

## Slide 20: Recall: Step-by-step Processor Design
3.3
Step 1: ISA => Logical Register Transfers
Step 2: Components of the Datapath
Step 3: RTL + Components => Datapath
Step 4: Datapath + Logical RTs => Physical RTs
Step 5: Physical RTs => Control

## Slide 21: Step 4: R-rtype (add, sub, . . .)
3.4
Logical Register Transfer
Physical Register Transfers
inst Logical Register Transfers
ADDU R[rd] <– R[rs] + R[rt]; PC <– PC + 4
inst Physical Register Transfers
IR <– MEM[pc]
ADDU A<– R[rs]; B <– R[rt]
S <– A + B
R[rd] <– S; PC <– PC + 4
Exec
Reg.
File
Mem
Access
Data
Mem
S
M
Reg
File
PC
Next PC
IR
Inst. Mem
Time
A
B

## Slide 22: Step 4: Logical immed
3.5
Logical Register Transfer
Physical Register Transfers
inst Logical Register Transfers
ORI R[rt] <– R[rs] OR ZExt(Im16); PC <– PC + 4
inst Physical Register Transfers
IR <– MEM[pc]
ORI A<– R[rs]; B <– R[rt]
S <– A or ZExt(Im16)
R[rt] <– S; PC <– PC + 4
Exec
Reg.
File
Mem
Access
Data
Mem
S
M
Reg
File
PC
Next PC
IR
Inst. Mem
Time
A
B

## Slide 23: step 4 : Load
3.6
Logical Register Transfer
Physical Register Transfers
inst Logical Register Transfers
LW R[rt] <– MEM[R[rs] + SExt(Im16)];
PC <– PC + 4
inst Physical Register Transfers
IR <– MEM[pc]
LW A<– R[rs]; B <– R[rt]
S <– A + SExt(Im16)
M <– MEM[S]
R[rd] <– M; PC <– PC + 4
Exec
Reg.
File
Mem
Access
Data
Mem
S
M
Reg
File
PC
Next PC
IR
Inst. Mem
A
B
Time

## Slide 24: Step 4 : Store
3.7
Logical Register Transfer
Physical Register Transfers
inst Logical Register Transfers
SW MEM[R[rs] + SExt(Im16)] <– R[rt];
PC <– PC + 4
inst Physical Register Transfers
IR <– MEM[pc]
SW A<– R[rs]; B <– R[rt]
S <– A + SExt(Im16);
MEM[S] <– B PC <– PC + 4
Exec
Reg.
File
Mem
Access
Data
Mem
S
M
Reg
File
PC
Next PC
IR
Inst. Mem
A
B
Time

## Slide 25: Step 4 : Branch
3.8
Logical Register Transfer
Physical Register Transfers
inst Logical Register Transfers
BEQ if R[rs] == R[rt]
then PC <= PC + 4+SExt(Im16) || 00
else PC <= PC + 4
Exec
Reg.
File
Mem
Access
Data
Mem
S
M
Reg
File
PC
Next PC
IR
Inst. Mem
inst Physical Register Transfers
IR <– MEM[pc]
BEQ E<– (R[rs] = R[rt])
if E then PC <– PC + 4 +SExt(Im16)||00
else PC <–PC+4
A
B
Time

## Slide 26: Today’s Topic
00
01. Introduction & Recap
02. Analyze the Single Cycle Microprocessor
03. Construct a Multi-Cycle Datapath
04. More details of the Multi-Cycle Datapath
05. Control
06. Exceptions
07. Summary

## Slide 27: Multi-Cycle Datapath in Textbook
4.1
Minimum Hardware: A memory and an adder

## Slide 28: Beginning of Ins Fetch
4.2

## Slide 29: End of Ins Fetch
4.3

## Slide 30: Ins Fetch Cycle
4.4

## Slide 31: Fetch Registers and Ins Decode
4.5
busA<=RegFile[rs]; busB<=RegFile[rt]
ALU is not in use: ALUctr=XX

## Slide 32: Fetch Registers and Ins Decode-Continued
4.5

## Slide 33: The end of branch instruction
4.6

## Slide 34: Instruction Decode: R-Type
4.7

## Slide 35: Execution of R-type
4.8

## Slide 36: Finish of R-Type
4.9

## Slide 37: Instruction Decode: Ori
4.10

## Slide 38: Execution of Ori
4.11

## Slide 39: Finish of Ori
4.12

## Slide 40: Instruction Decode: LW/SW
4.13

## Slide 41: Memory Address Calculating
4.14

## Slide 42: Memory Access for SW
4.15

## Slide 43: Memory Access for LW
4.16

## Slide 44: Write Back for LW
4.17

## Slide 45: Recap:Multi-Cycle Datapath in Textbook
Minimum Hardware: A memory and an adder

## Slide 46: Control FSM
4.18

## Slide 47: Today’s Topic
00
01. Introduction & Recap
02. Analyze the Single Cycle Microprocessor
03. Construct a Multi-Cycle Datapath
04. More details of the Multi-Cycle Datapath
05. Control
06. Exceptions
07. Summary

## Slide 48: Our Control Model
5.1
State specifies control points for Register Transfer
Transfer occurs upon exiting state (same falling edge)
Control State
Next State
Logic
Output Logic
inputs (conditions)
outputs (control points)
State X
Register Transfer
Control Points
Depends on Input

## Slide 49: Step 4  Control Specification for multicycle proc
5.2
IR <= MEM[PC]
R-type
A <= R[rs]
B <= R[rt]
S <= A fun B
R[rd] <= S
PC <= PC + 4
S <= A or ZX
R[rt] <= S
PC <= PC + 4
ORi
S <= A + SX
R[rt] <= M
PC <= PC + 4
M <= MEM[S]
LW
S <= A + SX
MEM[S] <= B
PC <= PC + 4
BEQ
PC <=
Next(PC,Equal)
SW
“instruction fetch”
“decode / operand fetch”
Execute
Memory
Write-back

## Slide 50: Traditional FSM Controller
5.3
State
6
4
11
next
State
op
Equal
control points
state
op
cond
next
state
control points
Truth Table
datapath State

## Slide 51: Step 5  (datapath + state diagram control)
5.4
Translate RTs into control points
Assign states
Then go build the controller

## Slide 52: Mapping RTs to Control Points
5.5
IR <= MEM[PC]
R-type
A <= R[rs]
B <= R[rt]
S <= A fun B
R[rd] <= S
PC <= PC + 4
S <= A or ZX
R[rt] <= S
PC <= PC + 4
ORi
S <= A + SX
R[rt] <= M
PC <= PC + 4
M <= MEM[S]
LW
S <= A + SX
MEM[S] <= B
PC <= PC + 4
BEQ
PC <=
Next(PC,Equal)
SW
“instruction fetch”
“decode”
imem_rd, IRen
ALUfun, Sen
RegDst,
RegWr,
PCen
Aen, Ben,
Een
Execute
Memory
Write-back

## Slide 53: Assigning States
5.6
IR <= MEM[PC]
R-type
A <= R[rs]
B <= R[rt]
S <= A fun B
R[rd] <= S
PC <= PC + 4
S <= A or ZX
R[rt] <= S
PC <= PC + 4
ORi
S <= A + SX
R[rt] <= M
PC <= PC + 4
M <= MEM[S]
LW
S <= A + SX
MEM[S] <= B
PC <= PC + 4
BEQ
PC <= Next(PC)
SW
“instruction fetch”
“decode”
0000
0001
0100
0101
0110
0111
1000
1001
1010
0011
1011
1100
Execute
Memory
Write-back

## Slide 54: (Mostly) Detailed Control Specification (missing0)
5.7
0000 ?????? ? 0001 1
0001 BEQ x 0011 1 1 1
0001 R-type x 0100 1 1 1
0001 ORI x 0110 1 1 1
0001 LW x 1000 1 1 1
0001 SW x 1011 1 1 1
0011 xxxxxx 0 0000 1 0 x 0 x
0011 xxxxxx 1 0000 1 1 x 0 x
0100 xxxxxx x 0101 0 1 fun 1
0101 xxxxxx x 0000 1 0 0 1 1
0110 xxxxxx x 0111 0 0 or 1
0111 xxxxxx x 0000 1 0 0 1 0
1000 xxxxxx x 1001 1 0 add 1
1001 xxxxxx x 1010 1 0 1
1010 xxxxxx x 0000 1 0 1 1 0
1011 xxxxxx x 1100 1 0 add 1
1100 xxxxxx x 0000 1 0 0 1 0
State Op field Eq Next IR PC Ops Exec Mem Write-Back
en sel A B E Ex Sr ALU S R W M M-R Wr Dst
R:
ORi:
LW:
SW:
-all same in machine
BEQ:
Rfetch
Dec:
IF:

## Slide 55: Performance Evaluation
5.8
What is the average CPI?
  state diagram gives CPI for each instruction type
  workload gives frequency of each type
Type CPIi for type Frequency CPIi x freqIi
Arith/Logic 4 40% 1.6
Load 5 30% 1.5
Store 4 10% 0.4
branch 3 20% 0.6
Average CPI: 4.1

## Slide 56: How Effectively are we utilizing our hardware?
5.9
Example: memory is used twice, at different times
  Ave mem access per inst = 1 + Flw + Fsw ~ 1.3
  if CPI is 4.8, imem utilization = 1/4.8, dmem =0.3/4.8
We could reduce HW without hurting performance
  extra control
IR <- Mem[PC]
A <- R[rs]; B<– R[rt]
S <– A + B
R[rd] <– S;
PC <– PC+4;
S <– A + SX
M <– Mem[S]
R[rd] <– M;
PC <– PC+4;
S <– A or ZX
R[rt] <– S;
PC <– PC+4;
S <– A + SX
Mem[S] <- B
PC <– PC+4;
PC < PC+4;
PC < PC+SX;

## Slide 57: Today’s Topic
00
01. Introduction & Recap
02. Analyze the Single Cycle Microprocessor
03. Construct a Multi-Cycle Datapath
04. More details of the Multi-Cycle Datapath
05. Control
06. Exceptions
07. Summary

## Slide 58: Exceptions
6
Exception = unprogrammed control transfer
  system takes action to handle the exception
    must record the address of the offending instruction
    record any other information necessary to return afterwards
  returns control to user
  must save & restore user state
Allows construction of a “user virtual machine”
normal control flow:
sequential, jumps, branches, calls, returns
user program
System
Exception
Handler
Exception:
return from
exception

## Slide 59: Two Types of Exceptions: Interrupts and Traps
6.1
Interrupts
  caused by external events:
    Network, Keyboard, Disk I/O, Timer
  asynchronous to program execution
    Most interrupts can be disabled for brief periods of time
    Some (like “Power Failing”) are non-maskable (NMI)
  may be handled between instructions
  simply suspend and resume user program
Traps
  caused by internal events
    exceptional conditions (overflow)
    errors (parity)
    faults (non-resident page)
  synchronous to program execution
  condition must be remedied by the handler
  instruction may be retried or simulated and program continued or program may be aborted

## Slide 60: Traps and Interrupts
6.2
exception means any unexpected change in control flow, without distinguishing internal or external;
Type of event From where? terminology I/O device request External Interrupt Invoke OS from user program Internal Trap Arithmetic overflow Internal Trap Using an undefined instruction Internal Trap

## Slide 61: What happens to Instruction with Exception?
6.3
MIPS architecture defines the instruction as having no effect if the instruction causes an exception.
When we get to virtual memory we will see that certain classes of exceptions must prevent the instruction from changing the machine state.
This aspect of handling exceptions becomes complex and potentially limits performance => why it is hard

## Slide 62: Precise Interrupts
6.4
Precise  state of the machine is preserved as if program executed up to the offending instruction
  All previous instructions completed
  Offending instruction and all following instructions act as if they have not even started
  Same system code will work on different implementations
  Difficult in the presence of pipelining, out-ot-order execution, ...
  MIPS takes this position
Imprecise  system software has to figure out what is where and put it all back together
Performance goals often lead designers to not implement precise interrupts
  system software developers, user, markets etc. usually wish they had not done this
Modern techniques for out-of-order execution and branch prediction help implement precise interrupts

## Slide 63: Big Picture: user / system modes
6.5
By providing two modes of execution (user/system) it is possible for the computer to manage itself
  operating system is a special program that runs in the privileged mode and has access to all of the resources of the computer
  presents “virtual resources” to each user that are more convenient that the physical resources
    files vs. disk sectors
    virtual memory vs physical memory
  protects each user program from others
  protects system from malicious users.
  OS is assumed to “know best”, and is trusted code, so enter system mode on exception.
Exceptions allow the system to taken action in response to events that occur while user program is executing:
  Might provide supplemental behavior (dealing with denormal floating-point numbers for instance).
  “Unimplemented instruction” used to emulate instructions that were not included in hardware

## Slide 64: Addressing the Exception Handler
6.6
Traditional Approach: Interrupt Vector
  PC <- MEM[ IV_base + cause || 00]
  370, 68000, Vax, 80x86, . . .
MIPS Approach: fixed entry
  PC <– EXC_addr
  Actually very small table
    RESET entry
    TLB
    other
iv_base
cause
handler
code
iv_base
cause
handler entry code

## Slide 65: Saving State
6.6
Push it onto the stack
  68k, 80x86
Shadow Registers
  M88k
  Save state in a shadow of the internal pipeline registers
Save it in special registers
  MIPS EPC, BadVaddr, Status, Cause

## Slide 66: Additions to MIPS ISA to support Exceptions?
6.7
Exception state is kept in “coprocessor 0”.
  Use mfc0 read contents of these registers
  Every register is 32 bits, but may be only partially defined
  BadVAddr (register 8)
  register contains memory address at which memory reference occurred
  Status (register 12)
  interrupt mask and enable bits
  Cause (register 13)
  the cause of the exception
  Bits 5 to 2 of this register encodes the exception type (e.g undefined instruction=10 and arithmetic overflow=12)
  EPC (register 14)
  address of the affected instruction (register 14 of coprocessor 0).
Control signals to write BadVAddr, Status, Cause, and EPC
Be able to write exception address into PC (8000 0180hex)
May have to undo PC = PC + 4, since want EPC to point to offending instruction (not its successor): PC = PC - 4

## Slide 67: Details of Status register
6.7
Mask = 1 bit for each of 6 hardware and 2 software interrupt levels
  1 => enables interrupts
  0 => disables interrupts
k = kernel/user
  0 => was in the kernel when interrupt occurred
  1 => was running user mode
e = interrupt enable
  0 => interrupts were disabled
  1 => interrupts were enabled
When interrupt occurs, 6 LSB shifted left 2 bits, setting 2 LSB to 0
  run in kernel mode with interrupts disabled
Status
15
8
5
4
3
2
1
0
k
e
k
e
k
e
Mask
old
prev
current

## Slide 68: Details of Cause register
6.7
Pending interrupt 6 hardware levels: bit set if interrupt occurs but not yet serviced
  handles cases when more than one interrupt occurs at same time, or while records interrupt requests when interrupts disabled
Exception Code encodes reasons for interrupt
  0 (INT) => external interrupt
  4 (ADDRL) => address error exception (load or instr fetch)
  5 (ADDRS) => address error exception (store)
  6 (IBUS) => bus error on instruction fetch
  7 (DBUS) => bus error on data fetch
  8 (Syscall) => Syscall exception
  9 (BKPT) => Breakpoint exception
  10 (RI) => Reserved Instruction exception
  12 (OVF) => Arithmetic overflow exception
Status
15
10
Pending
5
2
Code

## Slide 69: Example: How Control Handles Traps in our FSM
6.8
Undefined Instruction–detected when no next state is defined from state 1 for the op value.
  We handle this exception by defining the next state value for all op values other than lw, sw, 0 (R-type), jmp, beq, and ori as new state 12.
  Shown symbolically using “other” to indicate that the op field does not match any of the opcodes that label arcs out of state 1.
Arithmetic overflow–detected on ALU ops such as signed add
  Used to save PC and enter exception handler
External Interrupt – flagged by asserted interrupt line
  Again, must save PC and enter exception handler
Note: Challenge in designing control of a real machine is to handle different interactions between instructions and other exception-causing events such that control logic remains small and fast.
  Complex interactions makes the control unit the most challenging aspect of hardware design

## Slide 70: How to add traps and interrupts to state diagram
6.9
IR <= MEM[PC]
PC <= PC + 4
R-type
S <= A fun B
R[rd] <= S
S <= A op ZX
R[rt] <= S
ORi
S <= A + SX
R[rt] <= M
M <= MEM[S]
LW
S <= A + SX
MEM[S] <= B
SW
“instruction fetch”
“decode”
0000
0001
0100
0101
0110
0111
1000
1001
1010
1011
1100
BEQ
0010
If A = B
then PC <= S
S<= PC +SX
undefined
instruction
EPC <= PC - 4
PC <= exp_addr
cause <= 10 (RI)
other
S <= A - B
overflow
EPC <= PC - 4
PC <= exp_addr
cause <= 12 (Ovf)
EPC <= PC - 4
PC <= exp_addr
cause <= 0(INT)
Handle
Interrupt
Pending INT

## Slide 71: Summary
7
Disadvantages of the Single Cycle Processor
  Long cycle time
  Cycle time is too long for all instructions except the Load
Multiple Cycle Processor:
  Divide the instructions into smaller steps
  Execute each step (instead of the entire instruction) in one cycle
Partition datapath into equal size chunks to minimize cycle time
  ~10 levels of logic between latches
Follow same 5-step method for designing “real” processor